## Slide 1: Novel Method to Assess Motion Blur Kernel Parameters and Comparative Study of Restoration Techniques Using Different Image Layouts
Group Members:
Munira Akter Lata (1588)
Supriti Ghosh (2521)
Farjana Bobi (2379)
Supervisor:
Dr. Mohammad Abu Yousuf
Assistant Professor, IIT, JU

## Slide 2: Outline
1. Objective
2. Introduction
3. Degradation model of image
4. Proposed image restoration model
5. Experimental results
6. Comprehensive analysis of restoration techniques
7. Conclusion

## Slide 3: Objective
The main objective of our study is to introduce a new approach to increase efficiency of image restoration techniques by solving boundary value problem or artifacts of the blurred image.

## Slide 4: Introduction
The principal goal of our study is to reconstruct motion blurred image.
To improve restored image quality by removing boundary artifacts.
To apply non-blind restoration techniques for several image layouts such as .tif (Tag Index Format), .jpg (Joint Photographic Experts Group) and .png (Portable Network Graphics).
To determine which restoration technique is suitable for which kind of image layout.

## Slide 5: Proposed Image Restoration Model
Degraded Image
Boundary Artifacts Removal
Blur Direction Assessment
Blur Length Assessment
Image Restoration
Recovered Image
Efficiency Measure of Restoration Techniques

## Slide 6: Step 1: Degradation model
Original Image
f(x,y)
Motion Blur Kernel
d(x,y)
+
Degraded Image o(x,y)
Noise n(x,y)

## Slide 7: Step 2: Boundary Artifacts Removal of Blurred Image
Real blurred image has limited size but Fourier transform in restoration technique treats image size as infinite which is called as boundary value problem or boundary artifacts.
Boundary Artifacts Removal Model
Blurred Gray Level Image
Apply Hann Window
Remove Boundary Artifacts
Regain Blurred Gray Level Image O(x,y)

## Slide 8: Step 2: Boundary Artifacts Removal of Blurred Image
The coefficients of a Hann window are computes as follows:

## Slide 9: Step 3: Assessment of Blur Direction
ALGORITHM
Determine the Fourier transform O(k,l) of blurred image o(x,y).
Compute the log spectrum of O(k,l).
Calculate the Inverse Fourier transform (IFT) of log spectrum.
Detect the edge map of step 3.
Derived the accumulator array by using Hough transform.
Find the peak in Hough transform which corresponds to blur direction.

## Slide 10: Step 4: Assessment of Blur Length
ALGORITHM
Determine the Fourier transform O(k,l) of o(x,y).
Compute the log spectrum of O(k,l) and transform it in binary.
Binary spectrum is rotated in the direction opposite to the blur direction.
Collapse the 2-D data into 1-D data.
Calculate the Inverse Fourier transform of 1-D data in step 4.
Detect the blur length using the real part of first negative value.

## Slide 11: Step 5: Image restoration
5.1. Restoration Technique Based on Wiener Method
5.2. Restoration Technique Based on Lucy-Richardson Method

## Slide 12: 5.1. Restoration Technique Based on Wiener Method
Restoration technique based on Wiener method treats images and noise as random variables.
It’s transfer function is given by:
(k,l) =[ ] O(k,l)
(k,l)-Estimated image
O (k,l)-Degraded image
- Power spectrum of main image
- Power spectrum of Noise

## Slide 13: 5.2. Restoration Technique Based on Lucy-Richardson Method
Another type of non-blind image restoration technique is based on Lucy-Richardson method that possess iterative procedure.
This method maximizes probability of restored image when convolved with PSF. If is the observed value at pixel position ‘i’ in the restored image then, it can be given as

## Slide 14: Experimental Result 1 Detected blur direction and blur length for artificially blurred images without noise
Image Used | Blur Direction | Blur Length | Assessed Direction | Assessed Length
Bird.tif | 10 | 12 | 12 | 13
 | 20 | 18 | 20 | 19
 | 55 | 37 | 54 | 37
Quote.jpg | 30 | 21 | 30 | 21
 | 22 | 11 | 19 | 11
 | 45 | 37 | 45 | 37
Fruits.png | 11 | 9 | 9 | 12
 | 17 | 13 | 16 | 14
 | 33 | 19 | 34 | 19

## Slide 15: Experimental Result 2 Detected blur direction and blur length for artificially blurred images with noise
Image Used | Noise Density (dB) | Blur Direction (degree) | Blur Length | Assessed Direction | Assessed Length
Bird.tif | 33 | 20 | 11 | 16 | 11
 | 31 | 50 | 17 | 55 | 18
 | 10 | 30 | 14 | 29 | 14
Quote.jpg | 13 | 16 | 13 | 14 | 15
 | 20 | 35 | 11 | 46 | 10
 | 16 | 47 | 19 | 45 | 20
Fruits.png | 23 | 15 | 18 | 16 | 18
 | 30 | 45 | 18 | 45 | 18
 | 15 | 20 | 12 | 35 | 13

## Slide 16: Experimental Result 3
Restoration result for blurred Bird.tif image with blur direction 20° and length 19

## Slide 17: Experimental Result 4
Restoration result for Quote.jpg with blur direction 10° and length 11.

## Slide 18: Experimental Result 5
Restoration result for Fruits.png with blur direction 17° and length 13.

## Slide 19: Experimental Result 6
Restoration result for Bird.tif with blur direction 20 ̊,length 19 and noise density 20 dB

## Slide 20: Experimental Result 7
Restoration result for Quote.jpg with blur direction 10° and length 11 and noise density 23 dB.

## Slide 21: Experimental Result 8
Restoration result for Fruits.png with blur direction 17°, length 13 and noise density 24 dB.

## Slide 22: Experimental Result 9 Performance measure of restoration techniques
Image Used | Performance Metrics | Restoration Tech. Based on Wiener Method | Restoration Tech. Based on Lucy Method
Bird.tif with blur direction 20ᴼ and length 19 | MSE | 0.0042 | 0.0036
 | RMSE | 0.0647 | 0.0599
 | NMAE | 0.0429 | 0.0401
 | PSNR | 23.7539 | 24.4235
Quote.jpg with blur direction 10ᴼ and length 11 | MSE | 0.0116 | 0.0112
 | RMSE | 0.1079 | 0.1058
 | NMAE | 0.0734 | 0.0803
 | PSNR | 19.3388 | 19.5078
Fruits.png with blur direction 17ᴼ and length 13 | MSE | 0.0010 | 0.0011
 | RMSE | 0.0320 | 0.0328
 | NMAE | 0.0226 | 0.0234
 | PSNR | 29.9092 | 29.6722

## Slide 23: Comprehensive Analysis with Existing Studies
[1] This study (at el. R. Lokhande) considered only wiener based method to restore degraded image. There’s no idea about improvement of image quality.
[2] This study (at el. R.Fergus) considered only one single photograph. No approximation about another type of image layouts.
[3] This study (at el. Haruka Asai) about removal of Gaussian noise. No focusing about impulse noise that is frequent during image acquisition.
In our study
we represents two non-blind image restoration techniques based on Wiener method and Lucy-Richardson method. An image quality increasing method called Hann window also adopted.
Three different image layouts are considered and detect which restoration technique suitable for which image layout.
Impulse noise taken into account which is more frequent than Gaussian noise due to faulty sensor.

## Slide 24: Conclusion
We conclude as, estimated blur direction and blur length are very close to theoretical value.
Restored image quality improved by restoration technique due to boundary artifact removal of the blurred image.
Different restoration techniques are suitable for different kind of image layouts as shown in experimental results.

## Slide 25: References
[1] R. Lokhande, K. V. Arya, and P. Gupta. 2006. Identification of parameters and restoration of motion blurred images. In Proceedings of the 2006 ACM symposium on Applied computing (SAC ’06 ). ACM, New York, NY, USA, 301-305.
[2] R.Fergus, B. Singh, A. Hertzmann, S.T. Roweis, W.T. Freeman, “Removing Camera Shake from a single photograph,” In Proceedings of the 2006 ACM 0730-0301/06/0700-0787.
[3] Haruka Asai, Yuji Oyamada, Julien Pilet, Hideo Satio, “Cepstral analysis based blind deconvolution for motion blur,” 17th IEEE International Conference on Image Processing., 978-1-4244-7993-1/10, Hong Kong, September, 2010.
[4] Rafael C. Gonzalez, Richard E. Woods, “Digital Image Processing,” Prentice Hall, 2007.
[5] Anil. K. Jain, “Fundamental of Digital Image Processing,” Prentice Hall, 1996.

## Slide 26
Thank You.....